Profibus

# Device Description

Installation Procedure

- Open the zip file using an unzip utility.

- Extract all files to "c:\Temp".

- On the drive that PDM is installed, run DeviceInstall.exe located in the directory "Siemens\pdm\sim_pdm\deviceinstall".

- Click the Next button when program starts.

- Provide the Path to "c:\Temp\32MVM.devices" in the space provided.

- Select "Search in", and click the Next button.

- Select the device you wish to install the Device Description (DD) for, and click Finish.

In this case 3244MVM(PA)

- Once installation is complete close application.

The Device Description files have now been installed in the Siemens PDM tool and are ready for use.

Profibus

# GSD File

Installation Procedure

This procedure is for users of the Siemens Simatic Software, and PDM users.

- Copy the 3144a.gsd file into the "Sinec\ComPB.nt\GSD directory on the drive that the Siemens Simatic Software tools are installed.

- Using the Siemens Com_Profibus tool, under the File drop down menu run the Scan GSD files utility.

- Use the Documentation drop down menu run the station types\GSD files utility to verify that the GSD file has been included. The file entry will be under the Other section of the list. The entry should look like this:

## Family                  Station Type                     Order Number           Version              GSD File

Other                   3244 Temperature Tr                                            1.0                      3144A.GSD

When selecting the sensor type in the slave config window the device will appear in the Other category of the type list.

This procedure will place the GSD file into the list of Station types/GSD files. Once this is done the GSD file will automatically be used for the creation of the NCM database file.

Rosemount Inc.

8200 Market Blvd.

Chanhassen, MN   55317

1-800-999-9307               							  paddinst.doc, 2-7-00